## Slide 1: RSPT 2335
Module A
AIRWAY MANAGEMENT
Part 2b
Tracheal Airways

## Slide 2: Parts of Module A AIRWAY MANAGEMENT
Part 1 – Pharyngeal, Laryngeal & Esophageal Airways
Part 2 – Tracheal Airways
Part 3 – Airway Clearance
Part 4 - Advanced Airways
Part 5 - Airway Complications & Emergencies

## Slide 3: Major Topics
Oral Intubation
Ventilator Associated Pneumonia
Alternative Airways & Accessories
Exchanges & Extubation
Tracheostomy Airway Insertion & Changes
Humidity & Oxygenation
Alternative Airways & Accessories
Laryngectomy
Communication Devices
Decannulation
Home care

## Slide 4: Tracheostomy Airway Insertion and Changes

## Slide 5: Terminology
Tracheotomy - Procedure used to form an opening in the trachea.
The opening is the tracheostomy.
A tube (a tracheostomy tube) is then inserted and usually sutured in place for approximately one week.

## Slide 6
Shiley
Low pressure cuff (LPC) trach tube

## Slide 7: Insertion
Surgical
Percutaneous

## Slide 8
I. Surgical Tracheotomy
Usually cut through 1st, 2 or 3 cartilage
Surgical tracheostomy (5:36 min)
http://www.youtube.com/watch?v=Qc0tNXF8tU8

## Slide 9
Lubricated tube with obturator is passed through the tracheal stoma (tracheotomy)

## Slide 10: Percutaneous
Percutaneous dilational tracheostomy technique
  Often done at bedside and assisted by therapist.
  Lower cost with less complications.
Videotape: “Percutaneous Tracheostomy”
(9.5 minutes)
UltraPerc Tracheostomy with fiberoptic bronchoscopy (10:10 min)
http://video.smiths-medical.tv/services/player/bcpid784767379001?bckey=AQ~~,AAAAAEBRJ4w~,jnMMg6V5IsDF_lDBR0B4Jj6ceZ1yk6k2

## Slide 11: Percutaneous Tracheostomy

## Slide 12
An over the needle catheter is first inserted into the space between the cricoid cartilage and tracheal ring #1 or between ring #1 & #2 and then a wire guide is inserted through the catheter.

## Slide 13
A short introducing dilator is placed over the wire guide followed by progressively larger dilators until the opening is large enough to accommodate the trach tube.

## Slide 14: Tracheostomy Tube Position
Evaluate tube placement
  Radiology: Tip of tube is located in approximately same place as ETT
    2 -3 cm or 1 inch below the cords
    2 - 7 cm above the carina at T2 - T4 (2 - 3 in.)
    At the level of the aortic knob/notch
    Mid trachea
  Flange on tube should rest gently against skin and be tied securely. (Tubes do come in different lengths)

## Slide 15: Changing the trach tube
Lab Chapter 23
  Exercise 23.2.2– Tracheostomy Tube Insertion/Change

## Slide 16
For a patient who loses their trach tube…
Place mouth seal on 15mm connector of resuscitation bag and use to seal over stoma
Use a neonatal resuscitation mask over stoma

## Slide 17: Humidity and Oxygenation

## Slide 18: Spontaneous Breathing Choices (non-vent)

## Slide 19: Spontaneous Breathing Choices (non-vent)
Trach collar
  cold or heated nebulizer
Stoma cover
HME
  minimum of 30 mg/L humidity

## Slide 20
Stoma
Humidification & Protection

## Slide 21
Trach HME

## Slide 22
Thermovent O2
Humidification & Oxygenation of trach tubes
O2 flow Approx. %O2
2 52
4 57
6 59
8 60
10 60

## Slide 23
Portex Thermovent HME with O2

## Slide 24
HME not used:
Dehydration
Hypothermia
Small VT (should be 3 x HME deadspace)
During aerosol tx

## Slide 25: Ventilator Patient Choices:

## Slide 26: Ventilator Patient Choices:
HME
  minimum of 30 mg/L humidity
HME Booster
Heated water bath humidification

## Slide 28
Fisher & Paykel
Heated Water Bath (HWB)

## Slide 29: Alternative Airways and Accessories

## Slide 30: Sizes
Sizes are very confusing on tracheostomy tubes.
Tube number does not correlate to internal diameter like ETT.
LOOK AT BOX FOR TUBE SIZES.
Evaluate proper suction catheter size very carefully.

## Slide 31
Trach Tube Sizes
AGE
JACKSON, DCT, DFEN, LPC, FEN, CFS, CFN TUBE SIZES
OUTSIDE DIAMETER
(OD mm)
INSIDE DIAMETER
(ID mm)
Premature to newborn
000-00
4.5
2.5
Newborn to 6 months
0
5.0
5.0
6 - 18 months
1
5.5
3.5
18 months to 4 - 5 yrs
1 - 2
5.5 - 6.0
3.5 - 4.0
4 - 10 years
2 - 3
6.0 - 7.0
4.0 - 5.0
10 - 14 years
3 - 5
7.0 - 9.0
4.5 - 6.5
12 years to adult
6
7.0
12 years to adult
8
8.5
12 years to adult
10
9.0

## Slide 32
SINGLE CANNULA TRACHS (SCT)
TRACH SIZE
INTERNAL DIAMETER
TRACH SIZE
INTERNAL DIAMETER
5.0
5.0 mm
8.0
8.0 mm
6.0
6.0 mm
9.0
9.0 mm
7.0
7.0 mm
10.0
10.0 mm
LARYNGECTOMY TUBES (LGT)
TRACH SIZE
INTERNAL DIAMETER
TRACH SIZE
INTERNAL DIAMETER
6.0
6.8 mm
10.0
9.1 mm
8.0
8.3 mm

## Slide 33: Types of Tracheostomy Tubes
Low Pressure Cuff (LPC) reusable
Low Pressure Cuff (DCT) disposable
Cuffless (CFS)
Single cannula (SCT)
Extra Long (XLT)
Fenestrated (FEN) or (CFEN)
Jackson
Foam-cuff (Bivona or Kamen Wilkenson)
Water filled cuff (TTS)

## Slide 34
Shiley Low pressure cuff (LPC) trach tube
(reusable inner cannula)
Size & type

## Slide 35
2. Shiley
Disposable inner cannula (DCT) trach tube

## Slide 36: Trach Tubes
Cuffless (CFS)
  No cuff
  Used for non-ventilated patients
  Used for patients without aspiration problems
Single cannula (SCT)
  No inner cannula
  More common in pediatrics
  Allows for larger inner diameter and less airflow resistance

## Slide 37
5. Special anatomical situations
Proximal extended length
Distal extended length

## Slide 38: Wire Enforced Tubes
EXAMPLE: Bivona Mid-Range Aire-Cuff Hyperflex
  Adjustable flange: Temporary tube for extended length
  Adjustable length with locking flange
  Sizes 6, 7, 8 and 9
  Length 110 – 140 mm
  Blue pilot valve = fill with air and measure cuff pressures

## Slide 39: Bivona Mid-Range Aire-Cuff Hyperflex
Adjustable
Blue = air
Wire enforced = No MRI

## Slide 40: 6. Fenestrated Tubes
Tracheostomy tube with a hole in the posterior surface
Used to facilitate upper airway functions
  Speech
  Cough
  Valsalva
  Smell
  Taste
  blowing nose
Used to facilitate decannulation.

## Slide 41
J
M
N
H
O

## Slide 42
Steps for plugging
  Suction upper airway
  Deflate cuff as patient coughs
  Remove inner cannula
  Insert proper plug
  Place oxygen on patient’s face

## Slide 43
Steps for capping
  Suction upper airway
  Deflate cuff as patient coughs
  Remove inner cannula
  Replace with fenestrated inner cannula
  Place cap on inner cannula
  Place oxygen on patient’s face

## Slide 44: Fenestrated Tubes
Why do I absolutely have to open the fenestration port and deflate the cuff before capping (plugging) a trach tube?

## Slide 45: Fenestrated Tubes
Why do I absolutely have to open the fenestration port and deflate the cuff before capping (plugging) a trach tube?
  Simple – if you don’t – the patient will suffocate!!!!!!!

## Slide 46: Fenestrated Tubes
Why should I replace the solid inner cannula before I suction the fenestrated trach tube?

## Slide 47
Replace the solid inner cannula before suctioning the airway to prevent the catheter from protruding out the fenestration port and causing tissue trauma.

## Slide 48: Fenestrated Tubes
What should I do if I cannot remove the fenestrated inner cannula or get an inner cannula back in the trach tube?

## Slide 49
  Tissue may occasionally migrate into fenestration port preventing insertion or removal of the fenestrated inner cannula.
  Manipulate the entire tube slightly to loosen tissue but if unsuccessful or if bleeding begins, contact physician.

## Slide 50
7.
Egan
Fig. 33-1
Jackson tracheostomy tube made from silver.It has no cuff and no 15-mm adapter.
Obturator
Inner cannula
Outer cannula

## Slide 51: Metal tube (Jackson or Silver Holinger)
Made of sterling silver.
Not used very often in acute care because they are uncuffed and do not have a 15 mm connection needed for ventilation.
They are also hard and do not conform to the airway anatomy.
May be seen in long term trach patient or laryngectomy.

## Slide 52: Metal Tracheostomy Tube
Set up the patient’s room before a problem occurs :
  If it is a tracheostomy patient; be sure there is the proper size 15 mm adapter attached to the resuscitation bag and a (face) mask available in the room at all times
  If it is a laryngectomy patient; be sure there is the proper size 15 mm adapter attached to the resuscitation bag and also a (stoma) mouth seal/ or small mask attached to the resuscitation bag

## Slide 53: Metal tube (Jackson or Silver Holinger)
What do I do if I have to ventilate a patient with a metal trach tube (or any other cuffless trach tube)?

## Slide 54
If it is a tracheostomy patient
Attempt to bag through the tube (need 15mm adapter)
If leak is too big – remove the tube, cover the stoma and bag mask ventilate until a cuffed tube can be placed.
Insert a cuffed trach tube or small ET tube into the stoma & ventilate

## Slide 55
If it is a laryngectomy patient
Attempt to bag through the tube (need 15mm adapter)
If leak is too big – remove the tube, cover the stoma with the small mask or mouth seal and ventilate
Insert a cuffed laryngectomy tube or small ET tube into the stoma & ventilate

## Slide 56
8. Fig. 33-32 Foam cuff is deflated on insertion. The pilot tube is opened after the tube is in place.

## Slide 57: Foam cuff
It is often used when there has been difficulty maintaining a seal and ventilating possibly due to tracheal dilation.

## Slide 58: Foam cuff
INSERTION:
  Use a syringe to deflated the cuff which is filled with polyurethane foam before insertion
  Once in place, leave the cuff line open to atmospheric pressure to allow the cuff to conform to the shape of the trachea
  NOTE: There is no pilot balloon valve on the pilot balloon line.

## Slide 59: Precautions
Lubricate suction catheter before inserting to prevent hanging up on tube this silicon tube
Use trach wedge to disconnect equipment. Never twist the trach tube as distal trachea damage nay occur.

## Slide 60: Foam cuff
In cases of severe leaks, the pilot balloon line can be adapted in-line in the ventilator circuit so when the ventilator circuit pressurizes, the cuff is inflated to hold a seal.
  May accumulate moisture in cuff faster
  PEEP may cause increased gas pressure in the cuff on exhalation

## Slide 61
Foam cuff with inline adapter which inflates cuff during mechanical ventilation inspiratory pressure.

## Slide 62: Foam cuff
MAINTENANCE:
  Every 8 - 12 hours (Q shift) the cuff is deflated completely
    Removes any moisture or debris
    Checks for cloudy fluid and possible bacteria in cuff
    Checks integrity of the cuff
  Do not measure cuff pressure
    measure and document volume of air.
    If volume is increasing then the trachea may be enlarging

## Slide 63
9. Bivona TTS
(Tight To Shaft)
May reprocess for single patient use (steam autoclave)
Must use disconnect wedge to prevent tube damage
Inflate cuff with sterile water
Use MOV technique

## Slide 64
Bivona TTS
(Tight To Shaft)
Gives profile of cuffless when deflated
Cannot see floppy cuff = sterile water
http://video.smiths-medical.tv/services/player/bcpid784767379001?bckey=AQ~~,AAAAAEBRJ4w~,jnMMg6V5IsDF_lDBR0B4Jj6ceZ1yk6k2
Cuff visible (floppy) = air

## Slide 65: Trach Accessories

## Slide 66
Helps prevent ventilator circuit disconnects

## Slide 67: TrachGuard anti-disconnect devices

## Slide 68
Egan Fig. 33-36 Tracheostomy button.

## Slide 69
Tracheal Button
Accessories

## Slide 70
Trach Button - Measure thickness of anterior wall to determine the number of spacers needed for a comfortable fit.

## Slide 71
Kistner Button
Used to wean patients
from trach tube
Keeps stoma open
Has one-way valve so
patient inspires through
button and exhales
through upper airway

## Slide 72
http://www.youtube.com/watch?v=a3OH7uusHM8
Montgomery Tube

## Slide 73: Montgomery T-tube
Used after laryngotracheal surgery
  Used to maintain an adequate airway
  Used to provide support to the stenotic trachea
Maintenance:
  Can be suctioned
  Can have speaking valve added
http://www.youtube.com/watch?v=kmN9qEgKhR0

## Slide 74: Laryngectomy

## Slide 75: Laryngectomy
Used for patients who have had larynx removed
Special precautions necessary because patient does not have use of upper airway for conduction of air
  Be prepared to ventilate stoma (ped. mask, mouth seal…)
  Remove face mask from room
  Have replacement tube at bedside
  Put signs over bed indicating laryngectomy

## Slide 76: Laryngectomy Tubes

## Slide 77: Critical Thinking Question
You enter the room of a ventilator patient who has a laryngectomy. The ventilator alarms are sounding and the laryngectomy tube is lying on the bed. The patient has no spontaneous respirations.
Describe in detail what you would do.

## Slide 78: Laryngectomy
Attempt to ventilate the stoma (ped. mask, mouth seal…)
Replace soiled tube with spare tube at the bedside
In an emergency – a pediatric tube can be placed in the stoma

## Slide 79
For a patient who loses their trach tube…
Place mouth seal on 15mm connector of resuscitation bag and use to seal over stoma
Use a neonatal resuscitation mask over stoma

## Slide 80: Communication Devices

## Slide 81: Communication Aides
Fenestrated or uncuffed trach tubes
  Cap
  Plugs

## Slide 82
Speaking devices
What is the main drawback to speaking valves for trachs?
Make sure both you & the patient are prepared for speech.

## Slide 83: Speaking devices CAP
With cap, patient breaths in and out through upper airway.
Need fenestrated tube and fenestrated inner cannula
  May not be as well tolerated due to airway resistance
    Inspiration
    Exhalation
    Both.

## Slide 84
Steps for capping
  Suction upper airway
  Deflate cuff as patient coughs
  Remove inner cannula
  Replace with fenestrated inner cannula
  Place cap on inner cannula
  Place oxygen on patient’s face

## Slide 85: Speaking devices Plug
With plug, patient breaths in and out through upper airway.
Need fenestrated tube but not fenestrated inner cannula
  May not be as well tolerated due to airway resistance
    Inspiration
    Exhalation
    Both.

## Slide 86
Steps for plugging
  Suction upper airway
  Deflate cuff as patient coughs
  Remove inner cannula
  Insert proper plug
  Place oxygen on patient’s face

## Slide 87: Questions
SCENARIO: You have a spontaneous breathing trach patient on a 40% trach collar.
If you plug the trach, how do you administer the 40% oxygen?
  To the face: nasal cannula, air entrainment mask, aerosol mask…

## Slide 88: Communication Aides
b) One-way valves:
    Passy-Muir
    Phonate (Covidien)
  See directions for application to:
      Non-ventilated patient
      Ventilated patient
  See Performance Evaluation

## Slide 89: Speaking devices Valves
Speaking valves are used in place of plugs or caps
  Less airway resistance
    Allows inspiration through trach
    Allows exhalation through upper airway
Oxygen is usually place over the artificial airway

## Slide 90
Egan Fig. 33-28 Passy Muir family of valves including one that can be used to deliver oxygen to the tracheostomy patient.
Watch
Passy-Muir DVD
in class

## Slide 91
Passy-Muir Valves
Speech
Smell
Swallow
Airway clearance
May reduce aspiration

## Slide 92: Questions
SCENARIO: You have a spontaneous breathing trach patient on a 40% trach collar.
If you apply a Passy Muir valve, how do you administer the 40% oxygen?
  Trach collar

## Slide 93: Questions
SCENARIO: You have a tracheostomy patient preparing to go home on a ventilator. You want to begin teaching the patient to use a Passy Muir valve.
What are some of the problems associated with use of a Passy Muir valve on a ventilator patient?
  Loss of exhaled volume out upper airway
  Low tidal volume delivery due to leak
  Loss of PEEP
  Increased spontaneous respiratory rate to compensate for volume loss
  Increased CO2
  Desaturation from loss of MAP
  Ventilator alarms (low volume & pressure)
  Aspiration due to deflated cuff
  (See handout on proper procedure)

## Slide 94: Critical Thinking Question
Al Strachen is a 16-year-old quadriplegic with C-7 fracture caused by a diving accident. He is currently in a rehabilitation facility. He has a size 6 nonfenestrated tube in place. The physiatrist has requested that the nurse provide a tracheostomy adjunct to allow the patient to speak. The nurse obtained a Passy-Muir valve and attached it to the 15-mm adapter of the inner cannula. You were then called stat to evaluate the patient for severe respiratory distress.
Explain why the patient did not tolerate the procedure and what you would need to do to correct the situation.

## Slide 95: Other Communication Tools and Options
  Buttons
Talking Trach Tubes
Sign language
Computers (e-mail & telephone hook-ups)
Electro-larynx
Esophageal Speech or “Burp” talking
Surgery – TEP Prosthesis
  Tracheoesophageal Puncture

## Slide 96
Egan
Fig. 33-27 "Talking" tracheostomy tube.
Provide a gas flow of air or O2 above the cuff and through the cords to facilitate speech

## Slide 98: What if the patient does not have vocal cords??
Laryngectomy patients have options as well
  Electro-larynx
  Esophageal Speech or “Burp” talking
  Surgery – TEP Prosthesis
    Tracheoesophageal Puncture

## Slide 99
Electrolarynx

## Slide 100
Esophageal Speech

## Slide 101
Tracheoesophageal Puncture & Prosthesis (TEP)

## Slide 102: Decannulation

## Slide 103: Decannulation
Progressive decrease in size of trach tube
Change to fenestrated or uncuffed tube then cap or plug or use valve

## Slide 104: Swallow Testing
Before cuff is deflated or removed - assess aspiration risk:
  Obtain sterile water mixed with blue dye
  Suction the patient orally and deflate the cuff
  Suction the airway
  Have the trach patient drink some of the mixture
  Suction the airway again
    If blue dye is suctioned, the patient is aspirating

## Slide 105: Decannulation Process #1
Decrease in size of trach tube
  Change to progressively smaller/uncuffed tubes
  Eventually remove the tube
    Do not suture stoma
    Surgical closure is not usually needed
  Apply sterile dressing and possibly topical antibiotic
  Clean site periodically
  Encourage cough and breathing exercises

## Slide 106: Decannulation Process #2
Switch to fenestrated or uncuffed trach to get patient accustomed to use of upper airway.
  May add cap, plug or speaking valve
  Eventually remove tube
    Do not suture stoma
    Surgical closure is not usually needed
  Apply sterile dressing and possibly topical antibiotic
  Clean site periodically
  Encourage cough and breathing exercises

## Slide 107: Home Care

## Slide 108: Home Trach Care
Be sure all upper airway functions are understood and taken care of:
  Conducting air
  Warm gas
  Humidify gas
  Filter gas
  Protect airway

## Slide 109: Home Care
Arrange for home care equipment & supplies
  Medical Alert “Neck Breather”
  Trach care
  Suction
  Aerosol
  Oxygen or compressor
Instruct patient & family members

## Slide 110: Education
CONDUCTING AIR:
  Perform trach care
    Avoid use of harsh soaps or full strength peroxide as they can be irritating & increase coughing
  Suction airway
  Prepare a “GO” bag for traveling
  Use saline instillation as needed

## Slide 111: Education
WARM GASES:
  Avoid temperature extremes
  Stay inside in bad/cold weather
  Keep trach covered
    Wear lint free scarf, clean cotton t-shirt put on backwards, gauze, bib or HME

## Slide 112: Education
HUMIDIFY GAS:
  Drink extra fluids
  Use cool aerosol set-up
  Use HME
  Keep home humidified
  Stay indoors during extremely cold weather
  Keep trach covered

## Slide 113: Education
FILTERING:
  Use lint free cloths to clean trach (do not use tissues near trach)
  Keep trach covered
  Avoid fumes, aerosols, dust, airborne droplets, people with respiratory infections, insects

## Slide 114: Education
PROTECTION:
  Use caution when bathing and showering
  Avoid water sports
  Cover trach with plastic bib when showering
  Prevention – hand washing, equipment processing, clean technique…

## Slide 115: Education
Contact doctor or HC provider
  Monitor for symptoms – difficulty breathing, bleeding, fever, malaise, sputum change, redness, swelling, pain…