## Slide 1: RSPT 2335
Mechanical Ventilation
Module C
Management Lesson #2
Asthma

## Slide 2: MODULE C-2 - Assignments
READ:
  Review: Chapter 13 of Clinical Manifestations & Assessment of Respiratory Disease
  Pilbeam - See First Day Handout
Performance Evaluation

## Slide 3: MODULE C-2 - Resources
Optional videotapes (E-108):
  Professor’s Rounds 2007: NAEPP Asthma Care Guidelines Updated for 2007
  Professor’s Rounds: Sedation & Paralysis of the Ventilated Patient

## Slide 4: MODULE C-2 - Resources
Clinical Practice Guideline:
Aerosol Therapy:
  ACCP Device Selection and Outcomes of Aerosol Therapy: Evidence-Based Guidelines (2005)
Asthma:
  NAEPP EPR-3 2007 Asthma Guidelines
    (new guidelines due out soon)

## Slide 5: MODULE C-2 -Objectives
When you complete this module, you should be able to…
  describe the problems associated with asthma.
  discuss different methods for improving CO2 removal.
  demonstrate the techniques for administering aerosol therapy to a ventilated patient.
  explain how aerosol therapy, sedation, steroids, permissive hypercapnia and Heliox play a role in ventilation of the asthmatic patient.

## Slide 6: MODULE C-2 Major Topics
Asthma Summary
Non-invasive strategies
Invasive strategies to improve ventilation
Scenario

## Slide 7: Asthma Summary

## Slide 8
Asthma is a “chronic inflammatory disease”
What we already know…

## Slide 9
ANATOMIC CHANGES:
Airway & mucosal inflammation
Smooth muscle constriction
Smooth muscle hypertrophy*
Goblet cell increase
Mucus gland enlargement
Ciliary damage
Air trapping
SIGNS & SYMPTOMS:
Inspection:
  Tachypnea
  Prolonged exhalation
  Tachycardia
  Hypertension
  Pulsus Paradoxus
  Cyanosis
  Cough & sputum production
SIGNS & SYMPTOMS:
Inspection:
  Barrel chest
  Accessory muscle use & tripod use
  Pursed lip breathing
  Retractions
Palpation
  Decreased tactile fremitus
  Rhonchial fremitus
Percussion
  Hyperresonant percussion
Auscultation
  Wheezing & rhonchi
  Diminished breath, heart & vocal sounds (fremitus)

## Slide 10
DIAGNOSTICS
Abnormal PFT
  Decreased FVC, FEV1 & flows
  Increased RV & RV/TLC ratio
Lab value changes
  Increase eosinophils
  Charot-Leyden crystals (found in sputum from eosinophil breakdown)
  Kirschman spirals
  (spiral shaped mucus plugs)
  Elevated IgE levels (extrinsic)
DIAGNOSTICS
Abnormal ABG
  Initially: Acute alveolar hyperventilation with hypoxemia
  Severe: Acute ventilatory failure with hypoxemia
Abnormal x-ray *
  Flattened diaphragms
  Hyperlucent lung fields
  Long narrow heart
  Flattened ribs
  Increased retrosternal air space
  Atelectasis (from mucus plugging)

## Slide 11
  Flattened diaphragms
  Hyperlucent lung fields
  Long narrow heart
  Flattened ribs
  Increased retrosternal air space

## Slide 12: Goal of Therapy in ASTHMA
Empty the lungs!
  … just like Emphysema

## Slide 13: MODULE C Major Topics
Asthma Summary
Non-invasive strategies
Invasive strategies to improve ventilation
Scenario

## Slide 14: Non-invasive Management Strategies

## Slide 15: Non-invasive Management Strategies
Short term Oxygen therapy.
  Low (nasal cannula) & high flow (AEM & Vapotherm).
Patient positioning (head up, tri-pod).
Aerosol therapy.
  Beta 2 agonists, anticholinergics, methylxanthines, inhaled & IV steroids
Leukotriene inhibitors.
Heli-ox via non-rebreather mask.
IV Magnesium Sulfate.
Bronchial hygiene
  PEP Therapy, Acapella
Vaccines & antibiotics (as needed)
NIPPV via mouthpiece/mask(with aerosol therapy).

## Slide 16: Magnesium sulfate (MgSO4)
Considered as an adjunct therapy for severe and life-threatening asthma exacerbation.
Theoretically it can induce bronchial smooth muscle relaxation in a dose-dependent manner by inhibiting…
  calcium influx into the cytosol (the water-soluble components of cell cytoplasm, constituting the fluid portion that remains after removal of the organelles and other intracellular structures)
  histamine release from mast cells
  acetylcholine release from cholinergic nerve endings
It also may increase the bronchodilator effect of β2-agonist by increasing the receptor affinity.

## Slide 18: MODULE C Major Topics
Asthma Summary
Non-invasive strategies
Invasive strategies to improve ventilation
Scenario

## Slide 19: Invasive Management Strategies
Proper Ventilator Management
Therapeutics
Pharmacology agents in MV
Permissive Hypercapnea
Heli-ox
Bronchial Thermoplasty

## Slide 20: Proper Ventilator Management
Breath Type (volume or pressure)
Mode
Adjust tidal volume (low 5 – 8 mL/kg IBW or lower).
Reduce alveolar deadspace (air trapping).
Reduce mechanical deadspace.
Correct for circuit loss.
Adjust rate (</= 8 bpm).
Eliminate auto-PEEP.
Watch patient synchrony.
Allow for spontaneous breathing.

## Slide 21: Invasive Management Strategies
Proper Ventilator Management
Therapeutics
Pharmacology agents in MV
Permissive Hypercapnea
Heli-ox
Bronchial Thermoplasty

## Slide 22: Therapeutics
Aerosol therapy
Steroid use
Bronchial hygiene

## Slide 23: Aerosol Therapy
Deposition
  Dose
    Spontaneous breathing
      achieve 10 – 14% deposition
    Ventilator patient
      achieve 1.0 – 15.3% deposition
Why the great variation in dose delivery with the ventilated patient?

## Slide 24: We can’t agree on where, which or how.

## Slide 25: Methods of administering medication to improve ventilation
Things to consider:
  What is the size of the patient?
  What type of ventilator or O2 device is in use?
  What type of humidification?
  What type of aerosol generator?
  Is bias flow present?
  Is SVN flow intermittent or continuous?

## Slide 26: What does the latest evidence say???

## Slide 27
Ventilator without bias flow for flow triggering

## Slide 29
The Aeroneb Solo performance was 5-6 times superior to small volume nebulizers and outperformed all others at all locations.

## Slide 30: High Frequency Ventilation

## Slide 31: High Flow Nasal Cannula
Aeroneb

## Slide 32: Non-invasive ventilation

## Slide 33: Which nebulizer and how much drug to use?
Different Equipment:
In all studies, the Vibrating Mesh and MDI with spacer delivered more than twice as much medication as the SVN
2. Different drugs:

## Slide 34: SUMMARY
Placement for adults & peds on vent:
  MDI or SVN intermittent on insp. side of wye.
  SVN continuous or intermittent – always at ventilator.
    Continuous flow = reservoir.
    Cleaner (no secretions nebulized).
  Aeroneb
    Bias flow - At vent or humidifier.
    No bias flow – place on insp. side of wye

## Slide 35: SUMMARY
Placement for adults & peds :
  HFOV - Place all equipment between wye & ETT
  HFNC -
    MDI at nose
    Jet neb & Aeroneb – before humidifier
  NIV - MDI, Jet neb & Aeroneb – at mask

## Slide 36: MSRC 2014 - Fink
Placement for neonates on any type of ventilation (conventional or HFOV):
  MDI , Jet neb & Aeroneb – at patient airway between ET & Wye connector.

## Slide 37: Other Things to Improve Aerosol Deposition
Mode
  Encourage spontaneous breathing.
Tidal Volume
  Increase as much as possible (>500cc).
  Use of sigh is acceptable.
Respiratory Rate
  Decrease as much as possible.
Duty Cycle
  Increase inspiratory time as much as possible.
  Use of a plateau or inspiratory hold is controversial.
  Actuate during early insp. NOT end exhalation.
Place & Use Equipment Properly
  MDI, Chamber, Spacer, Nebulizer, Gas Flow...

## Slide 38: How do I know when I get the desired effect?
Dose Response Therapy
  Increasing the dosage to achieve the desired or optimal effect.
    Monitor for side effects.
    Monitor for hypokalemia & dysrhythmias.

## Slide 39: Assessing Response
Graphic Assessment
  Pressure – Time Curve
    Peak – plateau pressure difference*
    Airway resistance measurement
    Auto-PEEP Maneuver

## Slide 40
Compliance & Resistance

## Slide 41: Assessing Response
Graphic Assessment
  Flow-Time Curve (or flow-volume loop)
    Expiratory flow tracing
    Auto-PEEP maneuver

## Slide 43: Assessing Response
Patient Assessment
  Breath sounds
  Patient WOB
  Vital signs
  SpO2

## Slide 44
Consider Costs of Different Nebulizers

## Slide 45
Using an MDI

## Slide 46: Advantages associated with MDI
Faster & Possibly Cheaper (labor time).
As good or better than SVN when using spacer or VHC.
Does not add any flow so it does not alter.
  Trigger
  Vt.
  PIP
  Flow
  FIO2
  Alarm function
Does not contaminate & obstruct expiratory filter.

## Slide 47
Using an MDI
with any humidification system
on adult or pediatric
conventional ventilation.

## Slide 48
You must use a Large-volume spacers.
*improve inhaled aerosol deposition 4 – 6 fold over MDI adapters.

## Slide 49
Large-volume spacers
*improve inhaled aerosol deposition 4 – 6 fold over MDI adapters.

## Slide 50: HME or HME Booster
Placed spacer 2 – 6 inches from wye on inspiratory side.
Spacer can be left in place.
Remove HME or HME Booster before therapy and replace afterwards.

## Slide 51
HME
Spacer
MDI
ET tube
Proper placement of MDI Spacer when using any humidifier
Leave MDI spacer in inspiratory line & remove HME for treatment.
Remove HME

## Slide 52
Place on insp. side of wye

## Slide 53
HME Bypass System
Good way to prevent derecruitment

## Slide 54: Bypass HMEs
Placed spacer 2 – 6 inches from wye on inspiratory side.
Spacer can be left in place.
Do not need to remove or replace anything.
Adjust to “aerosol mode” for therapy and return to “HME mode” afterwards.

## Slide 55
Lever down = aerosol mode
Lever up = HME Mode

## Slide 56: Gibeck Humid-Flo 72-hour passive humidification
http://www.teleflex.com/en/usa/productAreas/respiratory/productGroups/ventilationManagement/products/gibeck-humid-flo/components/index.html#video-player

## Slide 57
Circuvent
HME Bypass System

## Slide 58: Heated Water Bath (active)
Placed spacer 2 – 6 inches from wye on inspiratory side.
Spacer can be left in place.
Do not need to remove or replace anything.

## Slide 59
Proper placement of MDI Spacer when using Heated Humidifier
Leave inline at inspiratory line before wye connector.
No need to break circuit
Heated Humidifier
Good way to prevent derecruitment

## Slide 60: Problems associated with MDI
Some organizations do not use the proper size spacers.
  Should be the size of toilet paper roll.
  Much more efficient than small adapters.
  Do not use elbows or closed suction adapters.
Some MDIs are not ventilator friendly (DPI, Respimat).
MDIs have become more expensive especially when used as single patient use canisters.
You may need to open circuit to give therapy. (remove HME)…
  Increased risk of VAP.
  Increased risk of derecruitment.

## Slide 61
HME/filter
Aerosol particles will impact against endotracheal tube. For neonates - use proper size spacer.
Do not use MDI here for adults or peds – only neonates.

## Slide 62
Do not use MDI port on closed suction system.
AARC CPG State:
7.6.1.2 Small-gauge adapters with closed suction devices. No published data support the use of these adapters.

## Slide 63
HME/filter
Do not use small adapters – use proper size spacer for adults and peds.

## Slide 64
Using a Small Volume Nebulizer (SVN).

## Slide 65
Using an SVN
with any humidification system
on adult or pediatric
conventional ventilation.

## Slide 66: Small Volume Nebulizers
Intermittent flow or continuous flow.
  Placed SVN 3 – 6 inches from ventilator outlet.
  Consider placing a filter in expiratory line if using continuous flow.
  Remove HME for therapy.

## Slide 67
#4 NEW GUIDELINE: 3 – 6 inched from ventilator outlet.

## Slide 68
HME
SVN in inspiratory line
Remove during tx.
Proper placement of nebulizer
Remove HME and add SVN & possibly Filter (F)
SVN
F

## Slide 69: Problems associated with SVN
May need to open circuit for therapy.
  Remove and replace HME.
  Place & remove SVN.
  New spring loaded SVN adapters can be left in line.
Takes a significant amount of time (labor costs).

## Slide 70: Problems associated with SVN
If using a continuous flow:
  Difficulty triggering (may need to increase rate).
  Change in FiO2
  Errors in flow & volume measurement.
  Increase in tidal volume.
  Increased pressures.
  Alarm malfunction.
  “Gummed up expiratory parts (filters).
  Loss (waste) of medication during exhalation.

## Slide 71
Using a Vibrating Mesh Nebulizer
with any humidification system
on adult or pediatric
conventional ventilation.

## Slide 72: Aeroneb Pro Nebulizer
The Aeroneb Pro overcomes the limitations posed by current methods of in-line aerosolization because it:
  increases deposition of drug in the lungs.
  eliminates ventilator interruption.
  does not interference with ventilator performance.
  Does not cause heat degradation of medication.

## Slide 73: Aeroneb Pro Nebulizer
Utilizing Aerogen’s OnQ™ Aerosol Generator, the Aeroneb Pro produces a fine particle, low velocity aerosol without environmentally unfriendly propellants, inefficient compressors or costly ultrasonic elements.
The Aeroneb Pro overcomes the issue of poor aerosol delivery during mechanical ventilation, depositing up to four times more medication through an endotracheal tube (in vitro) during mechanical ventilation than small volume nebulizers (SVNs).

## Slide 74
Proper placement of Vibrating Mesh Nebulizer such as AeroNeb Pro
VM
VM

## Slide 75: LET’S LOOK AT NEXT PERFORMANCE EVALUATION

## Slide 76: Invasive Management Strategies
Proper Ventilator Management
Therapeutics
Pharmacology agents in MV
Permissive Hypercapnea
Heli-ox
Bronchial Thermoplasty

## Slide 77: Therapeutics
Aerosol therapy
Steroid use
Bronchial hygiene

## Slide 78: Steroids
Systemic corticosteroids (Solu-Medrol)
  should be used cautiously in patients receiving steroidal based neuromuscular blocking agents (vercuronium bromide & pancuronium bromide) because of the potential of prolonged blockade.
  Prolonged paralysis
    can hinder weaning.
    Inhibit ability to ambulate for weeks or months.
Steroids & paralytics – bad combination.

## Slide 79: Bronchial Hygiene
Hydration
Suctioning
Other methods as indicated

## Slide 80: Invasive Management Strategies
Proper Ventilator Management
Therapeutics
Pharmacology agents in MV
Permissive Hypercapnea
Heli-ox
Bronchial Thermoplasty

## Slide 81: Pharmacology agents in MV
Pilbeam - Chapter 15:
Sedatives , Analgesics and Paralytics

## Slide 82: Sedatives & Analgesics
Uses:
  Anxiety
  Agitation
  Promote sleep
  Delirium
  Pain
Types:
  Benzodiazepines (valium, versed, ativan)
  Analgesics (opiods, morphine, fentanyl)
  Neuroleptics (haldol)
  Anesthetic Agents (propofol- diprivan)

## Slide 83: Levels of Sedation
Minimal
  responds to verbal commands.
Moderate
  requires more than verbal stimulation to respond
  conscious sedation.
Deep
  breathing may be affected.
Anesthesia
  usually unresponsive & ventilated.

## Slide 84: Sedatives (Benzodiazepines -valium, versed, ativan)
Indications:
  Reduce anxiety (anxiolysis)
  Provide amnesia (strong hypnotic)
  Induce sleep
  Improve tolerance of mechanical vent.
  Facilitate invasive procedures
  Decrease oxygen consumption
  Protect patient from self-injury

## Slide 85: Adverse reactions
Usual side effects:
  Confusion, Weakness, Dizziness, Drowsiness, Ataxia, Syncope, Vertigo, Amnesia
Unusual side effects
  CNS stimulation, restlessness, mania, euphoria, rage, sleep disorder
Withdrawal side effects:
  Severe anxiety, tachycardia, diaphoresis, hypertension, seizures…)
Respiratory side effects:
  Depression, apnea
Cardiovascular side effects:
  Decreases SV, CO, MAP, BP, SVR

## Slide 86: Narcotic analgesics (opioids - morphine, fentanyl)
Pain control for ICU patients is often inadequate.
Narcotic analgesics are used to control pain, allow early mobilization and decrease hospital stay.

## Slide 87: Narcotic analgesics
Agonists (morphine, codeine, meperidine or demerol and fentanyl)
  Most commonly used
Antagonist (naloxone or Narcan)
  Used to reverse narcotic OD

## Slide 88: Adverse effects
CNS – sedation, respiratory depression and atelectasis
Muscle groups - muscle twitching (myoclonus), convulsions, chest wall rigidity
CV – vasodilation, vagal bradycardia, hypotension
GI – delayed GI emptying, constipation, nausea
Others – contraction of pupils, altered levels of stress hormone, allergic reactions

## Slide 89: Narcotic analgesics considerations
Tolerance – need to increase dosage to obtain effective pain relief.
Physical dependence – evidence of withdrawal syndrome (irritability, joint pain, chills, hot flashes, anxiety, nausea, vomiting, lacrimation, rhinorrhea, diaphoresis, abdominal cramps, diarrhea
Psychological dependence – behavior of drug seeking, preoccupation with obtaining and using, drug use for other than pain (euphoria).

## Slide 90: Neuroleptics (haldol)
Used for extreme agitation and delirium
  disorganized thinking
  unnecessary motor activity
Whenever delirium is present, the route cause should be investigated

## Slide 91: Anesthetics – (propofol)
With anesthesia the patient is unresponsive and usually ventilated
Example:
  Diprivan
    Produces and maintains anesthesia
    Provides sedation in ventilator patients
    Does not provide analgesia (use pain meds)
Adverse effects
  Apnea, bradycardia, laryngospasm, bronchospasm, coughing, dyspnea, hypotension, burning or pain at infusion site, discolored urine
Monitoring in OR with Bispectral Index (BIS)

## Slide 92: Paralytics
Provide temporary paralysis of skeletal muscles.
Used in combination with sedative drugs and narcotic analgesics because perception & pain still exist. (awake & paralyzed)
Indications:
  Intubation
  Laryngeal spasm
  Surgery
  Mechanical ventilation

## Slide 93: Use in mechanical ventilation
Reduced combativeness & agitation.
Respiratory muscle relaxation.
Increased chest wall compliance.
Synchronization during unnatural modes.
Prevention of hypoxemia due to increased WOB.
Decreased ICP from excessive movement.

## Slide 94: Neuromuscular blocking agents
Depolarizing – prolongs the depolarization phase of muscle contraction. Muscle thinks ACh is present. Short acting
    Succinylcholine (Anectine, Quelicin)
Nondepolarizing – competes with acetylcholine (ACh) for the sites at the motor end plated, thus blocking the normal action of acetylcholine preventing depolarization. Long acting.
    Turbocurarine chloride (Tubarine)
    Pancuronium bromide (Pavulon) Depolarizing Agents

## Slide 95: Adverse effects
Apnea (set alarms carefully)
Loss of cough
Poor neurologic assessment
Emotional trauma (sedation needed)
Disuse atrophy
Pressure sores
Increased iatrogenic morbidity & mortality
Histamine release
CV side effects (tachy, brady, dysrhythmia...)

## Slide 96: Evaluation of NM blockade
Train-of-Four
  Peripheral nerve stimulator.
  Measures muscle twitch in response to stimulus.
Spontaneous muscle effort (> 5 seconds)
  Open eyes
  Head lift
  Protrude tongue
  Hand grip
Ventilation parameters
  MIP & VC
  ABG

## Slide 97
Train-of four (TOF) monitoring

## Slide 99: Invasive Management Strategies
Proper Ventilator Management
Therapeutics
Pharmacology agents in MV
Permissive Hypercapnea
Heli-ox
Bronchial Thermoplasty

## Slide 100: Permissive Hypercapnia
Strategy to minimize the occurrence of ventilator-related lung injuries caused by positive pressure ventilation.
  Barotrauma & pneumothorax is not uncommon in these patients
Accepting higher than normal PaCO2 so lung can be protected.
Hypoventilation usually results in a decreased pH (some as low as 7.10 but most >/= 7.20).
Often used for status asthmaticus and ARDS patients.

## Slide 101: Permissive Hypercapnia
PROCESS:
  Slow reduction of tidal volume to levels as low as 4 - 6 mL/kg IBW.
    Lower tidal volume slowly at 50 ml Q 20 – 30 min over a 12 - 24 hour period.
  Lower tidal volume or lower peak pressures.
  Keep Plateau pressures </= 30 cm H2O.

## Slide 102: Permissive Hypercapnia
PROCESS:
  Example of one guideline:
    PaCO2 allowed to rise up to 80 mmHg.
    Allow PaCO2 to increase no more than 10 mmHg per hour.
    pH usually kept >/= 7.20 with buffers.

## Slide 103: Permissive Hypercapnia (continued)
Attempt to normalize pH with buffers
  Bicarbonate (for resp. acidosis???)
    HCO3- + H+ = H2CO3 = CO2 + H2O
    Excreted by lungs
    Buffer effect greater than CO2 production effect
  Tris-hydroxymethyl-aminomethane (THAM)
    Binds with H+ and excreted by kidneys

## Slide 104: Permissive Hypercapnia (continued)
Complications of acidosis:
  CNS dysfunction
  Intracranial hypertension
  Neuromuscular weakness
  Cardiovascular instability
  Increase pulmonary vascular resistance
  Respiratory distress
  Electrolyte imbalance

## Slide 105: Permissive Hypercapnia (continued)
Complications of low tidal volume &/or low PIP
  Decreased MAP & oxygenation
  Atelectasis
  Patient discomfort
Patient may require increased FiO2, increased levels of PEEP and sedation

## Slide 106: 3. Invasive Management Strategies
Proper Ventilator Management
Therapeutics
Pharmacology agents in MV
Permissive Hypercapnea
Heli-ox
Bronchial Thermoplasty

## Slide 107: Heli-ox Therapy
Low-density breathing gas mixture.
Concentrations:
  60%/40% or 70%/30% or 80%/20%
May reduce airway resistance.
  1/3 density of air.
  Slight increase in viscosity.
  Decreased turbulence in flow.
  Decreased work of breathing.

## Slide 108: Heli-ox Therapy
Used to buy time while underlying upper airway problem resolves:
  Post extubation stridor
  Tracheobronchitis
  Croup
  Tracheal stenosis
  Extrinsic compression (tumor)
  Angioedema
  Vocal cord paralysis
  Foreign body

## Slide 109: Heli-ox Therapy
Used to buy time while underlying lower airway problem resolves:
  Asthma
  Bronchiolitis
  COPD
  Dyskinesia

## Slide 110: Heli-ox Therapy
Has been used with spontaneous breathing asthmatic patients.
  Decreased PaCO2
  Increased flow.
  Decreased resp. muscle fatigue (decrease WOB).
  Decreased pulsus paradoxus.
Has been used with intubated, mechanically ventilated asthmatic patients.
  Decreased PaCO2
  Decreased ventilating pressures.
  MDI recommended for aerosol therapy.

## Slide 111: Heli-ox Therapy
Drawbacks:
  Need special gas supply equipment.
    Mixed gas cylinders recommended (2 – 6 per 24 hours)
    He flowmeters & regulators recommended.
    If O2 flowmeter used a correction is made.
      60%/40% (flow times 1.4)
      70%/30% (flow times 1.6)
      80%/20% (flow times 1.8)

## Slide 112: Heli-ox Therapy
Drawbacks:
  Need special delivery equipment
    SPONTANEOUS: Well fitting non-rebreather.
    VENTILATOR: Flow sensors and volumes inaccurate so recommend pressure ventilation (Servo best).

## Slide 113: Heli-ox Therapy
Drawbacks:
  Limitation on oxygen use up to 40%.
  Expensive.
  Potential for suffocation if using separate gas cylinders and oxygen source lost.
  If used >24 hours it can cause hypothermia so warm gases to body temperature (He has high thermal conductivity).

## Slide 114: Heli-ox Therapy
Drawbacks with Mechanical Ventilation.
  Erroneous volume & flow measurements (low).
    Heated wire flow measuring devices are not recommended (Drager).
    Do not use Heliox with: NPB 840,
    Good ventilators are Servo 900C, 300A, Servo i
  Need active heated humidification with preferably heated wire.

## Slide 115: Heli-ox Therapy
Drawbacks with Mechanical Ventilation.
  Helium can interfere with:
    Trigger & Cycling
    Valve function & Gas mixing
    Leak compensation
    Monitors & Alarms (especially volume)
  Pressure ventilation may be more appropriate.

## Slide 116: Aptae’r Heliox Delivery System
Pressure support ventilator.
Works off pre-mixed heliox cylinders.
Has built in
  Aeroneb nebulizer system
  Rise time
  E-sen%
  Alarms

## Slide 117
Aptae’r Heliox Delivery System

## Slide 118: Invasive Management Strategies
Proper Ventilator Management
Therapeutics
Pharmacology agents in MV
Permissive Hypercapnea
Heli-ox
Bronchial Thermoplasty

## Slide 119: Bronchial Thermoplasty
Radiofrequency ablation of airway smooth muscle for sustained treatment of asthma.
Non-drug option for treatment.
Sunnyvale, Calif.-based Asthmatx Inc. received U.S. Food and Drug Administration approval on the use of the Alair Bronchial Thermoplasty System for treatment of severe persistent asthma in patients 18 and older whose asthma isn’t well controlled with inhaled corticosteroids and long-acting beta agonists.
The system is the first device-based asthma treatment approved by the FDA

## Slide 120: Bronchial Thermoplasty
Radiofrequency ablation (thinning) of airway smooth muscle for sustained treatment of asthma
For treatment of severe persistent asthma in patients 18 and older whose asthma isn’t well controlled with inhaled corticosteroids and long-acting beta agonists.
There is a sustained reduction in airway responsiveness to methacholine.

## Slide 121: Bronchial Thermoplasty Treatment
The procedure is well tolerated.
The procedure requires only light anesthesia
It can be performed on an outpatient basis.
Three thirty-minute treatments usually takes care of all accessible airways.

## Slide 122: Bronchial Thermoplasty Video
http://www.youtube.com/watch?v=m6WQLHTu53Y

## Slide 123: Bronchial Thermoplasty Treatment
A small, flexible tube called a bronchoscope is inserted through the nose or mouth and guided into the lungs.
Once the bronchoscope is situated in the desired airway, a catheter is inserted through the bronchoscope.
The tip of the catheter is inflated until it touches the sides of the airway wall.
Radio frequency energy is then sent through the catheter, heating the smooth muscle walls of the airway to approximately 149° F.
This temperature is sufficient to thin the smooth airway wall muscles without scarring or damaging them.

## Slide 124: Bronchial Thermoplasty
Two assumptions underlie the development of this procedure:
  ASM is a vestigial tissue.
  That treatment directed at ASM alone will provide sustained symptomatic and physiological improvement in asthmatic humans.

## Slide 125: Bronchial Thermoplasty Treatment
During an asthma attack, the smooth muscles of the airways contract.
Because bronchial thermoplasty thins the muscle walls, they cannot narrow as much when irritants trigger asthma attacks, resulting in less symptoms and asthma relief.
Participants in the bronchial thermoplasty study received three thirty-minute thermoplasty treatments that treated all accessible airways.

## Slide 126: MODULE C Major Topics
Asthma Summary
Non-invasive strategies
Invasive strategies to improve ventilation
Scenario